## Slide 1: Exploratory Seismic Data Analysis in the Field
Colton Kohnke
Advisor: Dave Hale
Colorado School of Mines
October 7, 2013

## Slide 2: The Problem
Only in the field for a short time
  Most of time is spent processing
  If survey geometry/parameters need to change, want to make the change sooner rather than later.
Want a way to efficiently explore survey geometry in an interactive way.

## Slide 3: The Project - JAVA Program
Store/Compute survey geometry
  Get station flags from handheld GPS
  Compute and display source/receiver locations for each FFID
  Use locations to lookup UTM Coordinates and use USGS digital elevation maps to lookup elevations
  Store information in an external spreadsheet

## Slide 4: The Project - JAVA Program
Display Survey Geometry
  Plot source/receiver midpoint in map view
  Select points using marque type tool and draw the seismic “line” through selected points
  Plot elevation profile along this line
  Use a slider to show points for each FFID
    Provides graphical history of seismic survey
    Will help catch mistakes

## Slide 5: The Project - JAVA Program
Interactively display seismograms
  Convert SEGD files to IEEE
  Display by FFID
  Display by midpoint within a defined region
  Display by offsets
Controls for
  Gain
  Amplitude balancing
  Zoom and scroll (provided by Mines JTK)

## Slide 6: The Project - JAVA Program
Simple processing
  Surface wave attenuation
  NMO Correction
  Integration with SU as a backend?
    Might cause compatibility problems

## Slide 8: Questions